OPCODE	DECRIPTION	EXAMPLE	RESPONSE
SETSMS	The sms value send protocol ,this protocol starts with "SETSMS" ,opcode next two char are number of sms to send , / next bytes are the sms numbers according to previos bytes all of the SMS numbers are must be max 16 char's and each of the number will seperate with an comma "," after that 6byte CRC and last 2 byte must be a <CR><LF> char "\r\n"	"SETSMS04+905554336744,+905554336743,+ 905554336742,+ 905554336741,0x8732"\r\n	If slave device able to achive get message properly it wil return an enum whilch will be , / OK-> 0 / FORMAT_ERR->1 / CRC_ERR->2 / UNKNOWN_ERR->3
SETSMSG	The message protocol starts with first the activation which is 2 char max number which indicate which sms will be actived / the numbers start from 0 to 63 (max 5 sms activation) 5 bit represent 5 sms max and the format is text for this. / 3 digit is the lenght of sms which can be max 236 char and after that 6byte CRC and last 2 byte must be a <CR><LF> char "\r\n"	"SETSMSG2065helloworld1helloworld2helloworld2helloworld3helloworl4helloworl50x2126"\r\n / NOT:20 ->10100 1'ler aftif sms nolar	If slave device able to achive get message properly it wil return an enum whilch will be , / OK-> 0 / FORMAT_ERR->1 / CRC_ERR->2 / MSG_LENGT_MISMACTH->3 / UNKNOWN_ERR->4
SETITIME	The message protocol starts with first the time interval of SMS which is 5 byte the number is in milisecond after that 5 byte for network time interval which is in millisecond also. after that 6byte CRC and last 2 byte must be a <CR><LF> char "\r\n	"SETITIME00500010000x6b2b"\r\n	If slave device able to achive get message properly it wil return an enum whilch will be , / OK-> 0 / FORMAT_ERR->1 / CRC_ERR->2 / UNKNOWN_ERR->3
SETNET	The sms value send protocol ,this protocol starts with "SETNET" ,opcode next two char are number of network to send, / next bytes are the nework ip no and port no ip numbers are must be max 15 char's and port names are 5 chars and each of the block will seperate with an comma "," after that 6byte CRC and last 2 byte must be a <CR><LF> char "\r\n	"SETNET02192.168.001.03008080,192.168.123.08098904,0xC03E"\r\n	If slave device able to achive get message properly it wil return an enum whilch will be , / OK-> 0 / FORMAT_ERR->1 / CRC_ERR->2 / UNKNOWN_ERR->3
SETNMSG	The message protocol starts with first the activation which is 2 char max number which indicate which sms will be actived / the numbers start from 0 to 63 (max 5 sms activation) 5 bit represent 5 sms max and the format is text for this. / 3 digit is the lenght of sms which can be max 236 char and after that 6byte CRC and last 2 byte must be a <CR><LF> char "\r\n"	"SETSMSG6365helloworld1helloworld2helloworld2helloworld3helloworl4helloworl50x2126"\r\n / NOT:20 ->11111 1'ler aftif network noları	If slave device able to achive get message properly it wil return an enum whilch will be , / OK-> 0 / FORMAT_ERR->1 / CRC_ERR->2 / MSG_LENGT_MISMACTH->3 / UNKNOWN_ERR->4